## Slide 1
ET AI HACKATHON 2026 · PHASE 2 · PROBLEM #2 — ENERGY SUPPLY-CHAIN RESILIENCE
KARNADHAR
कर्णधार — the helmsman who steers the ship through the storm
India imports 88% of its crude. Nearly half transits one strait. KARNADHAR is the AI command center that turns a 47-day supply crisis
into a decision made in 45 milliseconds — grade-by-grade, refinery-by-refinery.
Mann Sutariya · Pandit Deendayal Energy University, Gandhinagar
Assumptions reviewed with: Lydia Powell (ORF) · Prof. U. K. Bhui (PDEU)
Notes: Open: India runs on imported crude — 88%. Nearly half sails through a strait 3km wide at its narrowest. In June 2025 the world watched Hormuz almost close. KARNADHAR is our answer: an AI that watches the world, models the shock, and reroutes the country’s crude — in real time.

## Slide 2
THE PROBLEM
One strait can strangle the world’s 3rd-largest oil importer
88%
of India’s crude is imported
46%
transits the Strait of Hormuz — derived from official trade records, not assumed
9.5 days
of strategic reserve cover — voluntary, vs the IEA’s 90-day norm
+8%
Brent in a single session when Hormuz was threatened (June 2025)
And the real constraint isn’t barrels — it’s dollars. India is a twin-deficit economy. A sustained price shock adds ~$190 bn/yr to the import bill, blowing the current-account deficit from 1.2% to over 6% of GDP. Unlike trade-surplus Japan or Korea, India cannot sustain that dollar outflow — which is why unprepared economies take 47 days longer to stabilise supply (McKinsey). The data to act exists. The intelligence layer to act on it does not.
Sources: DGCIS trade records (May 2025–Apr 2026) · PPAC · ISPRL · EIA · twin-deficit framing reviewed with Lydia Powell, Distinguished Fellow, ORF
Notes: Four numbers tell the story. 88% imported. 46% through one strait — and we didn’t copy that number from a report, our system derives it from official customs records. Reserves: 9.5 days, voluntary. And when Hormuz was threatened last June, Brent jumped 8% in one session. The deep problem is the twin deficit — India cannot pay for expensive crude in dollars for long. That’s the insight an ORF Distinguished Fellow validated for us.

## Slide 3
THE INSIGHT EVERYONE MISSES
Crude oil is not fungible
Every other “resilience dashboard” treats oil as one number: barrels. Reality: a refinery is an engine tuned to a fuel. A deep-conversion coking refinery built for heavy, sour, asphaltene-rich crude physically cannot run ultra-light condensate — and a simple refinery cannot digest sour crude. When Hormuz closes, the question is not “where do we buy oil?” It is “which exact grade can each of our refineries actually run — and who has it?”
“That is — you are perfectly right.” Prof. U. K. Bhui, Petroleum Engineering, PDEU — on our refinery-constrained sourcing thesis. His guidance added the SARA dimension (asphaltenes) to our crude model.
WHAT DECIDES IF A BARREL IS RUNNABLE
API gravity — light vs heavy
Sulphur — sweet vs sour
Asphaltene (SARA) — coke precursor
SAME COUNTRY, DIFFERENT MACHINES
RIL Jamnagar Nelson 21.1 runs almost anything — needs heavy feed
BPCL/HPCL Mumbai Nelson 7.0 light, sweeter diet only — sour is a hard limit
Notes: Here is our wedge. Everyone modeling this problem treats oil as fungible. It is not. Three properties decide whether a refinery can run a barrel — API gravity, sulphur, and asphaltene content, the SARA insight Prof. Bhui gave us. Jamnagar with Nelson complexity 21 can digest nearly anything; Mumbai at Nelson 7 cannot touch sour crude. Any reroute plan that ignores this is fiction.

## Slide 4
WHAT WE BUILT
A multi-agent brain: signal → scenario → reroute → brief
SIGNAL
GDELT news agent +
live AIS ship tracking
→
SCENARIO
glass-box economic
cascade + twin deficit
→
REROUTE
grade-aware LP optimizer
over real refinery diets
→
BRIEF
executive decision memo,
numbers from the engine
REAL public data — no synthetic signals
Explicit, testable assumptions (every parameter named & editable)
Knowledge graph: supplier → route → chokepoint → refinery (50 nodes, 163 edges)
LLM writes words, never numbers — engine stays auditable
45 ms
end-to-end: signal to executable
recommendation
vs the 47-day average for economies without response intelligence
Notes: Four specialist agents chained by an orchestrator. The signal layer ingests real GDELT news and real AIS ship positions. The scenario layer is a glass-box economic cascade. The reroute layer is a real linear-programming optimizer over each refinery’s actual diet. And the briefing layer writes the memo — the LLM handles words, never numbers. The whole chain runs in 45 milliseconds.

## Slide 5
THE FOUNDATION
Built on official trade records — not synthetic data
Refinery (port) | MT/yr | Nelson | Hormuz exposure | Top real suppliers
RIL Jamnagar (Sikka + SEZ) | 76.3 | 21.1 | 43% | Russia 35 · Saudi 17 · Iraq 14
Nayara Vadinar | 41.7 | 11.8 | 29% | Russia 56 · Iraq 18 · Angola 6
IOCL Paradip | 34.8 | 12.2 | 50% | Iraq 24 · Russia 21 · UAE 14
HMEL Bathinda (Mundra) | 23.3 | 12.5 | 52% | Russia 32 · Saudi 18 · Iraq 16
BPCL/HPCL Mumbai | 23.2 | 7.0 | 60% | Saudi 25 · UAE 23 · US 21
BPCL Kochi | 12.4 | 8.0 | 54% | Russia 31 · UAE 23 · Iraq 16
46%
national Hormuz exposure —
DERIVED from customs data
10 × 36
refineries × supplier grades,
real volumes & landed prices
Every refinery’s crude diet, Hormuz dependence, and even its processing limits are grounded in what it actually imported — DGCIS port-wise records, PPAC capacities, public Nelson complexity, crude assay libraries.
DGCIS “India’s Import by Principal Commodity” May 2025–Apr 2026 · port→refinery mapping · country→grade assay mapping (crudemonitor/BP/ENI)
Notes: This table is the heart of our credibility. These are not estimates — this is what each refinery actually imported last year, from official customs records. Vadinar runs 56% Russian crude and is only 29% Hormuz-exposed. Mumbai is 60% exposed. Our headline 46% national exposure is computed from this data — most teams will quote a number from a report; we derive it.

## Slide 6
THE RESULT THAT MATTERS
The “fungible” plan is physically impossible. Ours is not.
NAIVE · “oil is oil”
INFEASIBLE
250 kb/d of ultra-light condensate assigned to deep coking refineries that physically cannot run it. A grade failure — not a logistics failure. This is the plan a fungible model would execute.
KARNADHAR · grade-aware LP
FEASIBLE
Every barrel runnable, sourced, within desulphurisation and asphaltene capacity. Heavy-sour rationed to the cokers (Jamnagar, Paradip); light-sweet routed to simple refineries (Mumbai, Chennai). Executable by a procurement desk.
$3.15 M/day
product yield protected by grade-matching
~$1.15 bn/yr
annualised value of that decision quality
1,370 kb/d
re-sourced across 10 refineries in one solve
Curated stress-demo (15 grades × 7 refineries, public assays) — the wedge REPRODUCES on the real DGCIS model: sulphur-blend breach at Vizag; 220 kb/d un-runnable under sanctions (next slides)
Notes: We ran the same crisis through two planners. The naive planner — price-rational, supply-respecting, but grade-blind — produces a plan where 250,000 barrels a day go to refineries that cannot process them. It is infeasible for a grade reason, which is exactly our thesis. KARNADHAR’s linear program produces a fully feasible plan and protects over 3 million dollars a day of product yield — over a billion dollars a year. And the same failure mode reproduces on the real customs-data model — different numbers, same physics, which is the point.

## Slide 7
EVALUATION FOCUS 1 · DISRUPTION SIGNAL DETECTION
We saw the June 2025 Hormuz crisis 12 days before the market
12 days
alert lead over the
Brent +8% session
200×
peak news coverage vs
quiet baseline (real GDELT)
Method: 10-day rolling baseline → alert when coverage sustains ≥3× baseline for 2 days. Simple, explainable, testable — and fused with live AIS tanker traffic (congestion flags at chokepoints) for multi-source confirmation.
Real GDELT DOC 2.0 coverage-volume series, cached 1–14 June 2025 · backtest vs 23 June Brent session · aisstream.io live vessel feed (Malacca verified live)
Notes: Our early-warning agent watches global news coverage of every chokepoint. In the real June 2025 data, coverage exploded to 200 times baseline. Our alert rule — deliberately simple and explainable — fired on June 11th, twelve days before the Brent 8% session. And it cross-confirms with live ship-tracking data.

## Slide 8
EVALUATION FOCUS 3 · SCENARIO MODEL FIDELITY
A glass-box cascade — ending in the deficit India cannot pay
₹125.5/L
retail fuel at full closure (+₹25.5)
−1.4 pp
GDP drag · +2.0 pp CPI
$191 bn/yr
extra import bill in USD
1.2% → 6.1%
current-account deficit, % of GDP
Every parameter is named, sourced and editable; sensitivity is one function call. “The binding constraint is the balance of payments, not the barrels” — the twin-deficit reframe came from our review with ORF.
Cascade: closure → net shortfall (after Saudi/UAE pipeline bypass) → Brent → import bill → pump price → CPI/GDP → CAD · reviewed with Lydia Powell, ORF
Notes: The brief demands explicit, testable assumptions — so our cascade is a glass box. Notice the flat segment: a 25% closure is absorbed by the Saudi and UAE bypass pipelines — the model knows that nuance. At full closure: Brent 190, petrol above 125 rupees, and the number that matters most — the current-account deficit exploding past 6% of GDP. India can’t sustain that dollar outflow. That’s why speed of response is a national-security variable.

## Slide 9
BEYOND ONE SCENARIO
Block any chokepoint. Sanction any supplier. Model it.
Hormuz full closure
naive: INFEASIBLE — blend breaches Vizag’s sulphur limit
KARNADHAR: FEASIBLE — and priced: the reroute ties up +66 VLCC-equivalents (ton-mile)
Hormuz + OPEC+ squeeze
alternate suppliers squeezed to 60% of headroom
still feasible — grade-matching value rises to $1.95M/day of protected yield
Russia sanctioned
naive sends 220 kb/d to refineries that cannot run it
usable shortfall 220 → 0 — India’s #1 supplier is replaceable, at a price
Hormuz + Russia (compound)
the nightmare: 3,900 kb/d gap, 2 of top 3 suppliers gone
honest: 2,166 kb/d unmet, quantified — naive pretends, with 546 kb/d of fake fill
An honest engine: when a shock is too severe to reroute around, KARNADHAR quantifies the gap instead of pretending — because “you must cut demand by X” is the most decision-useful output there is.
Notes: The engine generalizes — any chokepoint, any supplier sanction, any combination, all on the real customs-data model. Notice two things no dashboard gives you. First, honesty: in the compound shock the naive plan pretends to fill the gap with 546,000 barrels a day of crude the refineries cannot run; we count only usable barrels and state the true shortfall — 2,166. Second, the decision layer: the optimizer prices the reroute in tankers — plus 66 VLCC-equivalents — and its shadow prices name the scarcest barrel. That is what makes it usable for policy.

## Slide 10
EVALUATION FOCUS 4 · GEOSPATIAL INTELLIGENCE
The war-room: India’s energy lifeline, live on one screen
Live 3D globe true globe projection with real AIS vessels; refineries sized & coloured by real data
Cut vs alive routes every supply corridor recolours the instant a scenario changes
Knowledge-graph view toggle to the 50-node supplier→strait→refinery graph; threat edges glow per scenario
Multi-commodity lens same disruption scored across 8 strategic imports — Hormuz hits 53% of LNG too
Decision layer LP shadow prices, usable shortfall, VLCC ton-mile cost — live on every scenario
Notes: This is the product. Next.js and MapLibre over a FastAPI engine. The globe is live — the red routes are the Gulf corridors dying when Hormuz closes; the green ones are the alternates KARNADHAR is re-routing through. Click a scenario and the entire national plan re-solves in tens of milliseconds, measured live in-app. And under every scenario sits the decision layer: the LP’s shadow prices naming the scarcest barrel, the usable-shortfall honesty metric, and the tanker cost of longer voyages.

## Slide 11
WHY YOU CAN TRUST IT
Validated, evaluated, and reviewed by domain experts
AUTOMATED VALIDATION
45 / 45
checks passed — one command, exit-code gated, run in CI on every push
wedge holds: naive infeasible for grade reasons, LP optimal
cascade monotonic; bypass nuance; twin-deficit wired
signal alert precedes market repricing on real data
real-diet integrity: 46% exposure, configs sane
engine admits unmet demand under compound shocks
decision layer proven: shadow prices · VLCC ton-mile · usable shortfall
multi-commodity lens generalises (8 imports, one framework)
EVALUATION FOCUS — ALL FIVE, COVERED
EF-1 signal lead time: 12 days, real GDELT + AIS
EF-2 procurement executability: feasible, grade-matched plans
EF-3 scenario fidelity: explicit, testable, sensitivity-swept
EF-4 geospatial depth: live routed map, real diets
EF-5 response time: 45 ms signal → recommendation
EXPERT REVIEW
Lydia Powell — Distinguished Fellow, ORF: twin-deficit framing; SPR-as-voluntary-insurance; sourcing-first policy sequence. Prof. U. K. Bhui — Petroleum Engg., PDEU: wedge validated (“you are perfectly right”); SARA/asphaltene dimension added on his guidance.
Notes: Three layers of trust. A validation suite — 45 falsifiable assertions about the engine’s behaviour, all green, one command, and run automatically in CI on every push to the public repo. Full coverage of the brief’s five evaluation-focus criteria. And two independent domain experts — a Distinguished Fellow at ORF for the economics, and a PDEU petroleum professor for the refining science — reviewed our assumptions.

## Slide 12
BUSINESS IMPACT & SCALABILITY
Incumbents tell you what’s happening. We tell you what to do.
Kpler, Vortexa, S&P and Wood Mackenzie built a multi-billion-dollar market selling monitoring. KARNADHAR sells the decision layer — the feasible, grade-aware action plan — AI-native and India-first.
WHO PAYS
Refiners IOCL · BPCL · HPCL · RIL · Nayara
Traders desks living on disruption signals
Shippers & insurers chokepoint risk = pricing
Government PPAC · ISPRL · MoPNG — the anchor
THREE AXES OF SCALE
1 · Segments refiner → trader → insurer → sovereign (same engine, 7 buyer types)
2 · Geography 50+ import-dependent economies share this exact anatomy — Japan, Korea, Turkey, Philippines…
3 · Commodity demonstrated LIVE in-app: 8 strategic imports screened — LNG, pharma APIs, semiconductors… (Hormuz hits 53% of LNG)
Model: tiered SaaS — Monitor → Simulate → Orchestrate — plus API licensing. Land commercial desks first (months, not years); the sovereign deployment is the moat and the mission.
Notes: Is this a business? The market already pays billions for energy intelligence — Kpler, Vortexa, Wood Mackenzie. But they sell monitoring. We sell the decision. Seven buyer segments, starting with refiners and traders. Fifty-plus import-dependent countries share India’s anatomy. And the engine is commodity-agnostic — crude today, LNG and critical minerals tomorrow.

## Slide 13
NEXT 90 DAYS
Refinery configs calibrated with Prof. Bhui’s written inputs (in progress)
Commercial AIS feed for dense Gulf coverage; Claude-authored live briefs
Pilot conversations: PPAC · ISPRL — the analysis they do in days, in 45 ms
India’s energy lifeline has no helmsman for the storm.
Now it does.
KARNADHAR · Mann Sutariya · PDEU · mannsutaria2605@gmail.com
Notes: Close: everything you saw runs today — real data, real signals, provable results, expert-reviewed. India’s energy lifeline has no helmsman for the storm. Now it does. Thank you.